## Slide 1
Methods
Discussion
References
Objective
Results
Acknowledgements
What is a quantum computer [1]?
  Uses quantum bits (qubits) to process info
  Superposition allows the qubit to be in a state of one and zero simultaneously
  Entanglement “binds” a group of qubits together; their individual states are dependent on each other, no matter how far they are from each other
There are a few challenges that hinders quantum computers’ performance [2, 3]:
  Extremely susceptible to quantum noise, which can be anything from ambient temperature or local radiation from Wi-Fi
  Scalability issues—the largest processor was just unveiled by IBM: the 1,121-qubit Condor processor
  Relatively new field—in 1998, the first 2-qubit computer was built
Quantum gates
  Used to manipulate qubit states
  Analogous to classical logic gates like OR, NOT, etc.
  All gates are unitary operators, which mean they preserve state probability outcomes
  Reversible
Time series analysis can uncover underlying patterns
  Used to understand relationships and highlight trends between features and the error rate
  Common regression techniques can be used for analysis
    Root mean square error (RMSE) and coefficient of determination (R2) determine how accurate the predictions are
Introduction
Understanding the Influence of Qubit Features on Error Rates Henry Yu1 and Nicholas LaRacuente*,1 Dept. of Computer Science, Indiana University, Bloomington, IN USA
*corresponding author: nlaracu@iu.edu
Data Collection
  Qiskit, an SDK used for working with quantum computers, allows access to IBM machines [4]
  Accessed IBM system backends to retrieve data using Qiskit API [4]
    ibm_perth, a 7-qubit system based on Falcon processor; 315 days of data
    ibm_brisbane, ibm_cusco, ibm_kawasaki, ibm_kyoto, ibm_nazca, meibm_quebec, ibm_sherbrooke, 127-qubit systems based on Eagle processor; one day of data for each system
Preprocessing
  Qubit Features [5]
    decoherence time (T1 and T2)
    frequency, anharmonicity
    readout assignment error (prob meas0 prep1 and prob meas1 prep0) readout length
    gate time
    ID, rz, sx, Pauli-X (NOT gate), reset, √x gate errors
    controlled NOT (CNOT) gate error (exclusive to 7-qubit)
    ECR gate error (exclusive to 127-qubit)
  Scaled features to have standard deviation of 1
Time Series Analysis of CNOT Gate Error on ibm_perth
  LASSO regression is simple and allows for feature selection [6]
      = number of samples
      = input features (independent variables)
      = target value (what we are trying to predict; dependent variable)
      = coefficient vector
      = LASSO regularization
  Polynomial regression can capture nonlinear relationships [6]
    (quadratic order)
  Five-fold cross-validation (traditional 80-20 split)
    Dataset split into five subsets of approximately equal size
    Model trained on 80% (or 4/5 of the folds) and tested on remaining 20% (or remaining fold)
    Repeated five times using different training and testing combinations
  Predicted error for one CNOT gate over time
ECR Gate Error Prediction (127-qubit)
  Both linear and polynomial LASSO regression used again
  Five-fold cross-validation
  Predict one random ECR gate error
  Instead of across time, across different qubits on all systems
We aim to assess correlations between qubit features and ultimately predict error probability.
Time Series Analysis
  Optimal α-regularization = 0.07
    avg R2 score ≈ -1.252, which means model performs worse than just using the average of the predicted value
      Optimal R2 score is 1
    avg RMSE score ≈ 4.319x10-3, which is inconclusive since the range of values is small
      Optimal RMSE score is 0
  Results suggest qubit data over time is not predictive of error rate
ECR Prediction Across Qubits
  Optimal α-regularization = 0.11
    avg R2 score ≈ 0.105, which means model has weak predictive power, but is better than time analysis
    avg RMSE score ≈ 0.900, which is a very poor score because the range is very small
  Results suggest qubit data over other qubits is slightly predictive of error rate but still has poor score
Correlation Matrix
  Decoherence times (T1, T2) show negative relationship across variables
  Anharmonicity is neutral across all variables
  Shows that probability errors (prob meas0, prob meas1) and gate errors (Pauli-X, ECR) have a slight relationship
ECR Plot
  Negative ECR error caused by scaling the features
  Massive variation between predicted vs. actual values
  Outliers could have caused evaluation metrics (RMSE, R2) to score lower
  Suggests nonlinear relationship
We want to thank Dr. Paul Macklin and the Luddy School of Informatics, Computing, and Engineering.
We acknowledge the use of the IBM Quantum Services for this work.
Weak predictive power of qubit features for error rates for linear and low-order polynomials; stronger correlation among qubits compared to correlations across time
Limitations:
  Limited dataset for 7-qubit and extremely limited dataset for 127-qubit
  Dataset could contain lots of noise or improper cleaning
Next steps:
  Check the discrepancy between the correlation matrix and the error coefficients
    Correlation matrix suggests good relationship
    Error coefficients suggests bad relationship
Understanding relationships between qubit features and error rates may help mitigate errors in the future
[1] “What Is Quantum Computing?” Caltech Science Exchange, scienceexchange.caltech.edu/topics/quantum-science-explained/quantum-computing-computers. Accessed 6 Dec. 2023.
[2] Preskill, John. “Quantum Computing in the NISQ Era and Beyond.” Quantum, vol. 2, Aug. 2018, p. 79. Crossref, https://doi.org/10.22331/q-2018-08-06-79.
[3] Engdahl, Sylvia. “Noise in Quantum Computing.” Amazon, Greenhaven Press/Gale, 2008, aws.amazon.com/blogs/quantum-computing/noise-in-quantum-computing/
[4] Qiskit documentation. Version 0.45.0 https://docs.quantum.ibm.com/api/qiskit
[5] B. Baheri, Q. Guan, V. Chaudhary and A. Li, "Quantum Noise in the Flow of Time: A Temporal Study of the Noise in Quantum Computers," 2022 IEEE 28th International Symposium on On-Line Testing and Robust System Design (IOLTS), Torino, Italy, 2022, pp. 1-5, doi: 10.1109/IOLTS56730.2022.9897404.
[6] scikit-learn documentation. Version 1.3.2. https://scikit-learn.org/stable/modules/linear_model.html
1IBM Quantum
LaRacuente Lab
Undergraduate Research – Fall 2023
133-qubit Heron processor1
U43
correlation matrix visually represented by heatmap